## Slide 1: Pipelining
Data Hazard

## Slide 2: MIPS Execution Cycle
Obtain instruction from program storage (IF)
Determine required actions and registers (ID)
Compute result value or status (EX)
Deposit results in storage for later use (MEM)
Update Register File (WB)
Instruction
Fetch
Instruction
Decode
Execution
cycle
Memory
Access
Write Back Cycle

## Slide 3: Visualizing Pipelining

## Slide 4: Its Not That Easy for Computers
Limits to pipelining: Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: HW cannot support this combination of instructions (single person to fold and put clothes away)
  Data hazards: Instruction depends on result of prior instruction still in the pipeline (missing sock)
  Control hazards: Pipelining of branches & other instructionsstall the pipeline until the hazardbubbles” in the pipeline

## Slide 5: Speed Up Equation for Pipelining
CPIpipelined = Ideal CPI + Pipeline stall clock cycles per instr
Speedup = Ideal CPI x Pipeline depth Clock Cycleunpipelined
Ideal CPI + Pipeline stall CPI Clock Cyclepipelined
Speedup = Pipeline depth Clock Cycleunpipelined
1 + Pipeline stall CPI Clock Cyclepipelined
x
x

## Slide 6: Three Generic Data Hazards
InstrI followed by InstrJ
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it

## Slide 7: Three Generic Data Hazards
InstrI followed by InstrJ
Write After Read (WAR) InstrJ tries to write operand before InstrI reads I
  Gets wrong operand
Can’t happen in DLX 5 stage pipeline because:
  All instructions take 5 stages, and
  Reads are always in stage 2, and
  Writes are always in stage 5

## Slide 8: Three Generic Data Hazards
InstrI followed by InstrJ
Write After Write (WAW) InstrJ tries to write operand before InstrI writes it
  Leaves wrong result ( InstrI not InstrJ )
Can’t happen in DLX 5 stage pipeline because:
  All instructions take 5 stages, and
  Writes are always in stage 5

## Slide 9: Forwarding to Avoid Data Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11

## Slide 10: HW Change for Forwarding

## Slide 11: Data Hazard Even with Forwarding
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Notes: MIPS actutally didn’t interlecok: MPU without Interlocked Pipelined Stages

## Slide 12: Data Hazard Even with Forwarding
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9

## Slide 13: Software Scheduling to Avoid Load Hazards
Try producing fast code for
a = b + c;
d = e – f;
assuming a, b, c, d ,e, and f in memory.
Slow code:
LW Rb,b
LW Rc,c
ADD Ra,Rb,Rc
SW a,Ra
LW Re,e
LW Rf,f
SUB Rd,Re,Rf
SW d,Rd
Fast code:
LW Rb,b
LW Rc,c
LW Re,e
ADD Ra,Rb,Rc
LW Rf,f
SW a,Ra
SUB Rd,Re,Rf
SW d,Rd