## Slide 1: Chapter 3: Authentication, Authorization, and Accounting
CCNA Security v2.0

## Slide 2: Chapter Outline
3.0 Introduction
3.1 Purpose of the AAA
3.2 Local AAA Authentication
3.3 Server-Based AAA
3.4 Server-Based AAA Authentication
3.5 Server-Based Authorization and Accounting
3.6 Summary

## Slide 3: Section 3.1: Purpose of the AAA
Upon completion of this section, you should be able to:
Explain why AAA is critical to network security.
Describe the characteristics of AAA.

## Slide 4: Topic 3.1.1: AAA Overview

## Slide 5: Authentication without AAA
Telnet is Vulnerable to Brute-Force Attacks
The simplest method of remote access authentication is to configure a login and password combination on console, vty lines, and aux ports, as shown in Figure 1. This method is the easiest to implement, but it is also the weakest and least secure. This method provides no accountability. Anyone with the password can gain entry to the device and alter the configuration.
Notes: 3.1.1.1 Authentication without AAA

## Slide 6: Authentication without AAA (Cont.)
SSH and Local Database Method
SSH is a more secure form of remote access. It requires both a username and a password, both of which are encrypted during transmissions.
The local database method provides additional security, because an attacker is required to know a username and a password.
It also provides more accountability, because the username is recorded when a user logs in.
Although Telnet can be configured using a username and password, both are sent in plaintext, which makes it vulnerable to being captured and exploited.
Notes: 3.1.1.1 Authentication without AAA

## Slide 7: AAA Components
Network and administrative AAA security in the Cisco environment has three functional components:
Notes: 3.1.1.2 AAA Components

## Slide 8: Topic 3.1.2: AAA Characteristics

## Slide 9: Authentication Modes
Local AAA Authentication
Server-Based AAA Authentication
Notes: 3.1.2.1 Authentication Modes

## Slide 10: Authorization
AAA Authorization
Notes: 3.1.2.2 Authorization

## Slide 11: Accounting
Types of accounting information:
Network
Connection
EXEC
System
Command
Resource
AAA Accounting
AAA Accounting collects and reports usage data. This data can be used for such purposes as auditing or billing. The collected data might include the start and stop connection times, executed commands, number of packets, and number of bytes.
Network accounting captures information for all Point-to-Point Protocol (PPP) sessions, including packet and byte counts.
Connection accounting captures information about all outbound connections made from the AAA client, such as Telnet or SSH.
EXEC accounting captures information about user EXEC terminal sessions (user shells) on the network access server, including username, date, start and stop times, and the access server IP address.
System accounting captures information about all system-level events (for example, when the system reboots or when accounting is turned on or off).
Command accounting captures information about the EXEC shell commands for a specified privilege level that are being executed on a network access server. Each command accounting record includes a list of the commands executed for that privilege level, as well as the date and time each command was executed, and the user who executed it.
The Cisco implementation of AAA accounting captures "start" and "stop" record support for calls that have passed user authentication. The additional feature of generating "stop" records for calls that fail to authenticate as part of user authentication is also supported. Such records are necessary for users employing accounting records to manage and monitor their networks.
Notes: 3.1.2.3 Accounting
3.1.2.4 Activity - Indentify the Characteristics of AAA

## Slide 12: Section 3.2: Local AAA Authentication
Upon completion of this section, you should be able to:
Configure AAA authentication, using the CLI, to validate users against a local database.
Troubleshoot AAA authentication that validates users against a local database.

## Slide 13: Topic 3.2.1: Configuring Local AAA Authentication with CLI

## Slide 14: Authenticating Administrative Access
Add usernames and passwords to the local router database for users that need administrative access to the router.
Enable AAA globally on the router.
Configure AAA parameters on the router.
Confirm and troubleshoot the AAA configuration.
Notes: 3.2.1.1 Authenticating Administrative Access

## Slide 15: Authentication Methods
Notes: 3.2.1.2 Authentication Methods

## Slide 16: Default and Named Methods
Example Local AAA Authentication
The default keyword means that the authentication method applies to all lines, except those for which a specific line configuration overrides the default.
The authentication is case-sensitive, indicated by the local-case keyword. This means that both the password and the username are case sensitive.
Notes: 3.2.1.3 Default and Named Methods

## Slide 17: Fine-Tuning the Authentication Configuration
Show Unique ID of a Session
Display Locked Out Users
Command Syntax
Notes: 3.2.1.4 Fine-Tuning the Authentication Configuration

## Slide 18: Topic 3.2.2: Troubleshooting Local AAA Authentication

## Slide 19: Debug Options
Debug Local AAA Authentication
Notes: 3.2.2.1 Debug Options

## Slide 20: Debugging AAA Authentication
Understanding Debug Output
Notes: 3.2.2.2 Debugging AAA Authentication

## Slide 21: Section 3.3: Server-Based AAA
Upon completion of this section, you should be able to:
Describe the benefits of server-based AAA.
Compare the TACACS+ and RADIUS authentication protocols.

## Slide 22: Topic 3.3.1: Server-Based AAA Characteristics

## Slide 23: Comparing Local AAA and Server-Based AAA Implementations
Server-based authentication:
User establishes a connection with the router.
Router prompts the user for a username and password.
Router passes the username and password to the Cisco Secure ACS (server or engine)
The Cisco Secure ACS authenticates the user.
Local authentication:
User establishes a connection with the router.
Router prompts the user for a username and password, authentication the user using a local database.
Notes: 3.3.1.1 Comparing Local AAA and Server-Based AAA Implementations

## Slide 24: Introducing Cisco Secure Access Control System
Cisco Secure ACS supports both TACACS+ and RADIUS protocols, as shown in the figure. TACACS+ and RADIUS are the two predominant protocols used by Cisco security appliances, routers, and switches for implementing AAA.
Notes: 3.3.1.2 Introducing Cisco Secure Access Control System

## Slide 25: Topic 3.3.2: Server-Based AAA Communication Protocols

## Slide 26: Introducing TACACS+ and RADIUS
ARA – AppleTalk Remote Access.
NetBEUI - NetBIOS Extended User Interface. Is an enhanced version of the NetBios protocol that is used by Microsoft Windows networking. It is a non-routable protocol, which means that computers that are not located on the same network segment or subnet can't communicate.
Notes: 3.3.2.1 Introducing TACACS+ and RADIUS

## Slide 27: TACACS+ Authentication
TACACS+ Authentication Process
Notes: 3.3.2.2 TACACS+ Authentication

## Slide 28: RADIUS Authentication
RADIUS Authentication Process
Notes: 3.3.2.3 RADIUS Authentication

## Slide 29: Integration of TACACS+ and ACS
Cisco Secure ACS
Notes: 3.3.2.4 Integration of TACACS+ and ACS

## Slide 30: Integration of AAA with Active Directory
Microsoft Active Directory (AD) is a directory service for Windows domain networks, and is part of most Windows Server operating systems. The AD domain controller is used to enforce security policies by authenticating and authorizing users when they log into the Windows domain. Microsoft AD can also be used to handle authentication and authorization on Cisco IOS devices.
Although Cisco Secure ACS can be integrated to use the AD service, Microsoft Windows Server can also be configured as a AAA server. The Microsoft implementation of a AAA server using RADIUS is known as Internet Authentication Service (IAS). However, starting with Windows Server 2008, IAS has since been renamed Network Policy Server (NPS).
Notes: 3.3.2.5 Integration of AAA with Active Directory
3.3.2.6 Video - Integration of AAA with Identity Service Engine
3.3.2.7 Activity - Identify the AAA Communication Protocol

## Slide 31: Section 3.4: Server-Based AAA Authentication
Upon completion of this section, you should be able to:
Configure server-based AAA authentication, using the CLI, on Cisco routers.
Troubleshoot server-based AAA authentication.

## Slide 32: Topic 3.4.1: Configuring Server-Based Authentication with CLI

## Slide 33: Steps for Configuring Server-Based AAA Authentication with CLI
Enable AAA.
Specify the IP address of the ACS server.
Configure the secret key.
Configure authentication to use either the RADIUS or TACACS+ server.
Notes: 3.4.1.1 Steps for Configuring Server-Based AAA Authentication with CLI

## Slide 34: Configuring the CLI with TACACS+ Servers
Server-Based AAA Reference Topology
Configure a AAA TACACS+ Server
Use the single-connection command to enhance TCP performance by maintaining a single TCP connection for the life of the session. Otherwise, by default, a TCP connection is opened and closed for each session.
Notes: 3.4.1.2 Configuring the CLI for TACACS+ Servers

## Slide 35: Configuring the CLI for RADIUS Servers
Configure a AAA RADIUS Server
By default, Cisco routers use port 1645 for the authentication and port 1646 for the accounting. However, IANA has reserved ports 1812 for the RADIUS authentication port and 1813 for the RADIUS accounting port. It is important to makes sure these ports match between the Cisco router and the RADIUS server.
Notes: 3.4.1.3 Configuring the CLI for RADIUS Servers

## Slide 36: Configure Authentication to Use the AAA Server
Configure Server-Based AAA Authentication
Command Syntax
Notes: 3.4.1.4 Configure Authentication to Use the AAA Server
Syntax Checker - Configure Server-Based AAA Authentication

## Slide 37: Topic 3.4.2: Troubleshooting Server-Based AAA Authentication

## Slide 38: Monitoring Authentication Traffic
Troubleshooting Server-Based AAA Authentication
When AAA is enabled, it is often necessary to monitor authentication traffic and troubleshoot configurations.
The debug aaa authentication command is a useful AAA troubleshooting command because it provides a high-level view of login activity, as shown in the figure.
The command indicates a status message of PASS when a TACACS+ login attempt is successful. If the status message returned is FAIL, verify the secret key and troubleshoot as necessary.
Notes: 3.4.2.1 Monitoring Authentication Traffic

## Slide 39: Debugging TACACS+ and RADIUS
Troubleshooting RADIUS
Troubleshooting TACACS+
Notes: 3.4.2.2 Debugging TACACS+ and RADIUS

## Slide 40: Debugging TACACS+ and RADIUS (Cont.)
AAA Server-Based Authentication Failure
AAA Server-Based Authentication Success
Notes: 3.4.2.2 Debugging TACACS+ and RADIUS (Cont.)
3.4.2.3 Video Demonstration: Configure a Cisco Router to Access a AAA RADIUS Server

## Slide 41: Section 3.5: Server-Based AAA Authorization and Accounting
Upon completion of this section, you should be able to:
Configure server-based AAA authorization.
Configure server-based AAA accounting.
Explain the functions of 802.1x components.

## Slide 42: Topic 3.5.1: Configuring Server-Based AAA Authorization

## Slide 43: Introduction to Server-Based AAA Authorization
Authentication vs. Authorization
Authentication ensures a device or end-user is legitimate
Authorization allows or disallows authenticated users access to certain areas and programs on the network.
TACACS+ vs. RADIUS
TACACS+ separates authentication from authorization
RADIUS does not separate authentication from authorization
Notes: 3.5.1.1 Introduction to Server-Based AAA Authorization

## Slide 44: AAA Authorization Configuration with CLI
Example AAA Authorization
Authorization Method Lists
Command Syntax
Notes: 3.5.1.2 AAA Authorization Configuration with CLI

## Slide 45: Topic 3.5.2: Configuring Server-Based AAA Accounting

## Slide 46: Introduction to Server-Based AAA Accounting
Notes: 3.5.2.1 Introduction to Server-Based AAA Accounting

## Slide 47: AAA Accounting Configuration with CLI
Example AAA Accounting
Accounting Method Lists
Command Syntax
Notes: 3.5.2.2 AAA Accounting Configuration with CLI
Syntax Checker - Configure AAA Accounting

## Slide 48: Topic 3.5.3: 802.1X Authentication

## Slide 49: Security Using 802.1X Port-Based Authentication
802.1X Message Exchange
802.1X Roles
Notes: 3.5.3.1 Security Using 802.1X Port-Based Authentication

## Slide 50: 802.1X Port Authorization State
Command Syntax for dot1x port-control
Notes: 3.5.3.2 802.1X Port Authorization State

## Slide 51: Configuring 802.1X
Notes: 3.5.3.3 Configuring 802.1X
Syntax Checker - Configure 802.1X Port-Authentication on a 2960 Switch
3.6.1.1 Packet Tracer - Configure Authentication on Cisco Routers
3.6.1.2 Lab - Securing Administrative Access Using AAA and RADIUS

## Slide 52: Section 3.6: Summary
Chapter Objectives:
Explain how AAA is used to secure a network.
Implement AAA authentication that validates users against a local database.
Implement server-based AAA authentication using TACACS+ and RADIUS protocols.
Configure server-based AAA authorization and accounting.
Notes: 3.6.1.1 Packet Tracer - Configure Authentication on Cisco Routers
3.6.1.2 Lab - Securing Administrative Access Using AAA and RADIUS
3.6.1.3 Summary

## Slide 54: Instructor Resources
Remember, there are helpful tutorials and user guides available via your NetSpace home page. (https://www.netacad.com)
These resources cover a variety of topics including navigation, assessments, and assignments.
A screenshot has been provided here highlighting the tutorials related to activating exams, managing assessments, and creating quizzes.
1
2
Notes: https://www.netacad.com