## Slide 1: Chapter 5: Implementing Intrusion Prevention
CCNA Security v2.0

## Slide 2: Chapter Outline
5.0 Introduction
5.1 IPS Technologies
5.2 IPS Signatures
5.3 Implement IPS
5.4 Summary

## Slide 3: Section 5.1: IPS Technologies
Upon completion of this section, you should be able to:
Explain zero-day attacks.
Understand how to monitor, detect and stop attacks.
Describe the advantages and disadvantages of IDS and IPS.

## Slide 4: Topic 5.1.1: IDS and IPS Characteristics

## Slide 5: Zero-Day Attacks
A zero-day attack, sometimes referred to as a zero-day threat, is a computer attack that tries to exploit software vulnerabilities that are unknown or undisclosed by the software vendor, as shown in Figure 1. The term zero-hour describes the moment when the exploit is discovered.
Notes: 5.1.1.1 Zero Day Attacks

## Slide 6: Monitor for Attacks
Advantages of an IDS:
Works passively
Requires traffic to be mirrored in order to reach it
Network traffic does not pass through the IDS unless it is mirrored
One approach to prevent worms and viruses from entering a network is for an administrator to continuously monitor the network and analyze the log files generated by the network devices. This solution is not very scalable. Manually analyzing log file information is a time-consuming task and provides a limited view of the attacks being launched against a network. By the time the logs are analyzed, the attack may have already been successful.
Notes: 5.1.1.2 Monitor for Attacks

## Slide 7: Detect and Stop Attacks
IPS:
Implemented in an inline mode
Monitors Layer 3 and Layer 4 traffic
Can stop single packet attacks from reaching target
Responds immediately, not allowing any malicious traffic to pass
An IPS builds upon IDS technology. However, an IPS device is implemented in inline mode. This means that all ingress and egress traffic must flow through it for processing. As shown in the figure, an IPS does not allow packets to enter the trusted side of the network without first being analyzed. It can detect and immediately address a network problem.
Notes: 5.1.1.3 Detect and Stop Attacks

## Slide 8: Similarities Between IDS and IPS
Notes: 5.1.1.4 Similarities Between IDS and IPS

## Slide 9: Advantages and Disadvantages of IDS and IPS
Advantages IDS:
No impact on network
No network impact if there is a sensor failure
No network impact if there is a sensor overload
Advantages IPS:
Stops trigger packets
Can use stream normalization techniques
Disadvantages IDS:
Response action cannot stop trigger
Correct tuning required for response actions
More vulnerable to network security evasion techniques
Disadvantages IPS:
Sensor issues might affect network traffic
Sensor overloading impacts the network
Some impact on network
Stream normalization is a technique used to reconstruct the data stream when the attack occurs over multiple data segments.
Notes: 5.1.1.5 Advantages and Disadvantages of IDS and IPS
A normalizer is an inline network element that thwarts evasion attempts by removing ambiguities in network traffic. A particularly challenging step in normalization is the sound detection of inconsistent TCP retransmissions, wherein an attacker sends TCP segments with different payloads for the same sequence number space to present a network monitor with ambiguous analysis. Normalizers that buffer all unacknowledged data to verify the consistency of subsequent retransmissions consume inordinate amounts of memory on high-speed links.

## Slide 10: Topic 5.1.2: Network-Based IPS Implementations

## Slide 11: Host-Based and Network-Based IPS
There are two primary kinds of IPSs available: host-based and network-based.
Notes: 5.1.2.1 Host-Based and Network-Based IPS

## Slide 12: Network-Based IPS Sensors
Notes: 5.1.2.2 Network-Based IPS Sensors

## Slide 13: Cisco’s Modular and Appliance-Based IPS Solutions
Cisco IPS AIM and Network Module Enhanced (IPS NME)
Cisco ASA AIP-SSM
Cisco IPS 4300 Series Sensors
Cisco Catalyst 6500 Series IDSM-2
Advanced Inspection and Prevention Security Services Module (AIP-SSM)
As a standalone device, such as a Cisco IPS 4300 Series Sensor
Added to a Catalyst 6500 switch using an Intrusion Detection System Services Module (IDSM-2)
On an ISR router
Notes: 5.1.2.3 Cisco’s Modular and Appliance-Based IPS Solutions, Figures 1 - 4
5.1.2.4 Cisco’s Modular and Appliance-Based IPS Solutions (Cont.)

## Slide 14: Choose an IPS Solution
Factors affecting the IPS sensor selection and deployment:
Amount of network traffic
Network topology
Security budget
Available security staff to manage IPS
Small implementations such as branch offices might only require a Cisco IOS IPS-enabled ISR router. As traffic patterns increase, the ISR can be configured to offload IPS functions using an IPS NME or IPS AIM.
Larger installations can be deployed using an existing ASA 5500-X appliance.
Enterprises and service providers might require a dedicated IPS appliance or a Catalyst 6500 using an IDSM-2 network module.
Notes: 5.1.2.5 Choose an IPS Solution

## Slide 15: IPS Advantages and Disadvantages
Notes: 5.1.2.6 IPS Advantages and Disadvantages

## Slide 16: Modes of Deployment
Inline Mode
Promiscuous Mode
Cisco IDS and IPS sensors can operate in inline mode (also known as inline interface pair mode) or promiscuous mode (also known as passive mode).
Notes: 5.1.2.7 Modes of Deployment

## Slide 17: Topic 5.1.3: Cisco Switched Port Analyzer

## Slide 18: Port Mirroring
Traffic Sniffing Using a Switch
Traffic Sniffing Using a Hub
Notes: 5.1.3.1 Port Mirroring

## Slide 19: Cisco SPAN
Notes: 5.1.3.2 Cisco SPAN

## Slide 20: Configuring Cisco SPAN Using Intrusion Detection
Cisco SPAN Commands:
Monitor session command – used to associate a source port and a destination port with a SPAN session.
Show monitor command – used to verify the SPAN session.
Notes: 5.1.3.3 Configuring Cisco SPAN Using Intrusion Detection

## Slide 21: Section 5.2: IPS Signatures
Upon completion of the section, you should be able to:
Understand IPS signature characteristics
Explain IPS signature alarms
Manage and monitor IPS
Understand the global correlation of Cisco IPS devices

## Slide 22: Topic 5.2.1: IPS Signature Characteristics

## Slide 23: Signature Attributes
A signature is a set of rules that an IDS and an IPS use to detect typical intrusion activity.
Signatures have three distinct attributes:
Type
Trigger (alarm)
Action
Notes: 5.2.1.1 Signature Attributes

## Slide 24: Signature Types
Signatures are categorized as either:
Atomic – this simplest type of signature consists of a single packet, activity, or event that is examined to determine if it matches a configured signature. If yes, an alarm is triggered and a signature action is performed.
Composite – this type of signature identifies a sequence of operations distributed across multiple hosts over an arbitrary period of time.
For example, a LAND attack has an atomic signature because it sends a spoofed TCP SYN packet (connection initiation) with the same source and destination IP address of the target host and the same source and destination port as an open port on the target, as shown in the figure. The reason a LAND attack works is because it causes the machine to reply to itself continuously.
Notes: 5.2.1.2 Signature Types

## Slide 25: Signature File
As new threats are identified, new signatures must be created and uploaded to an IPS.
A signature file contains a package of network signatures.
Notes: 5.2.1.3 Signature File

## Slide 26: Signature Micro-Engines
Cisco IOS defines five micro-engines:
Atomic – Signatures that examine simple packets.
Service – Signatures that examine the many services that are attacked.
String - Signatures that use regular expression-based patterns to detect intrusions.
Multi-string – Supports flexible pattern matching and Trend Labs signatures.
Other – Internal engine that handles miscellaneous signatures.
To make the scanning of signatures more efficient, Cisco IOS software relies on signature micro-engines (SMEs), which categorize common signatures in groups. Cisco IOS software can then scan for multiple signatures based on group characteristics, instead of one at a time.
Notes: 5.2.1.4 Signature Micro-Engines

## Slide 27: Download a Signature File
Notes: 5.2.1.5 Acquire the Signature File
5.2.1.6 Activity – Identify IPS Signature Type

## Slide 28: Topic 5.2.2: IPS Signature Alarms

## Slide 29: Signature Alarm
Notes: 5.2.2.1 Signature Alarm

## Slide 30: Pattern-Based Detection
Notes: 5.2.2.2 Pattern-Based Detection

## Slide 31: Anomaly-Based Detection
Notes: 5.2.2.3 Anomaly-Based Detection

## Slide 32: Policy-Based and Honey Pot-Based Detection
Honey pot-based detection uses a dummy server to attract attacks. The purpose of the honey pot approach is to distract attacks away from real network devices.
By staging different types of vulnerabilities in the honey pot server, administrators can analyze incoming types of attacks and malicious traffic patterns. They can then use this analysis to tune their sensor signatures to detect new types of malicious network traffic.
Honey pot systems are rarely used in production environments. Antivirus and other security vendors tend to use them for research.
Notes: 5.2.2.4 Policy-Based and Honey Pot-Based Detection

## Slide 33: Benefits of the Cisco IOS IPS Solution
Benefits:
It uses underlying routing infrastructure to provide an additional layer of security.
It is inline and is supported on a broad range of routing platforms.
It provides threat protection at all entry points to the network when used in combination with Cisco IDS, Cisco IOS Firewall, VPN, and NAC solutions
The size of the signature database used by the devices can be adapted to the amount of available memory in the router.
Notes: 5.2.2.5 Benefits of the Cisco IOS IPS Solution

## Slide 34: Alarm Triggering Mechanisms
Understanding Alarm Types:
False Positive
True Positive
Alarm Attack Traffic
Notes: 5.2.2.6 Alarm Triggering Mechanisms
5.2.2.7 Activity – IPS Signature Alarms

## Slide 35: Topic 5.2.3: IPS Signature Actions

## Slide 36: Signature Actions
Summary of Action Categories:
Notes: 5.2.3.1 Signature Actions
Verbose = using or expressed in more words than are needed.

## Slide 37: Manage Generated Alerts
Generating an Alert:
Notes: 5.2.3.2 Manage Generated Alerts

## Slide 38: Log Activities for Later Analysis
Logging the Activity:
Notes: 5.2.3.3 Log Activities for Later Analysis

## Slide 39: Deny the Activity
Dropping or Preventing the Activity:
Notes: 5.2.3.4 Deny the Activity

## Slide 40: Reset, Block, and Allow Traffic
Resetting the Connection and Blocking the Activity:
Notes: 5.2.3.5 Reset, Block, and Allow Traffic
5.2.3.6 Activity – Identify the IPS Signature Action

## Slide 41: Topic 5.2.4: Manage and Monitor IPS

## Slide 42: Monitor Activity
IPS Planning and Monitoring Considerations:
Management method
Event correlation
Security staff
Incident response plan
Notes: 5.2.4.1 Monitor Activity

## Slide 43: Monitoring Considerations
Notes: 5.2.4.2 Monitoring Considerations

## Slide 44: Secure Device Event Exchange
IPS sensors and Cisco IOS IPS generate alarms when an enabled signature is triggered. These alarms are stored on the sensor and can be viewed locally, or through a management application, such as IPS Manager Express.
When an attack signature is detected, the Cisco IOS IPS feature can send a syslog message or an alarm in Secure Device Event Exchange (SDEE) format, as shown in the figure.
Notes: 5.2.4.3 Secure Device Event Exchange

## Slide 45: IPS Configuration Best Practices – refer to curicullum
Notes: 5.2.4.4 IPS Configuration Best Practices

## Slide 46: Topic 5.2.5: IPS Global Correlation

## Slide 47: Cisco Global Correlation
Goals of global correlation:
Dealing intelligently with alerts to improve effectiveness
Improving protection against known malicious sites
Sharing telemetry data with the SensorBase Network to improve visibility of alerts and sensor actions on a global scale
Simplifying configuration settings
Automatic handling of security information uploads and downloads
In addition to maintaining signature packs, Cisco IPS includes a security feature called Cisco Global Correlation. With global correlation, Cisco IPS devices receive regular threat updates from a centralized Cisco threat database called the Cisco SensorBase Network.
The Cisco SensorBase Network contains real-time, detailed information about known threats on the Internet. The goals of the Cisco Global Correlation are shown in the figure.
Notes: 5.2.5.1 Cisco Global Correlation

## Slide 48: Cisco SensorBase Network
Notes: 5.2.5.2 Cisco SensorBase Network
Telemetry = the process of recording and transmitting the readings of an instrument.

## Slide 49: Cisco Security Intelligence Operation
Network participation gathers the following data:
Signature ID
Attacker IP address
Attacker port
Maximum segment size
Victim IP address
Victim port
Signature version
TCP options string
Reputation score
Risk rating
Notes: 5.2.5.3 Cisco Security Intelligence Operation

## Slide 50: Reputations, Blacklists, and Traffic Filters
Notes: 5.2.5.4 Reputations, Blacklists, and Traffic Filters
5.2.5.5 Reputations, Blacklists, and Traffic Filters (Cont.)

## Slide 51: Reputations, Blacklists, and Traffic Filters
Notes: 5.2.5.4 Reputations, Blacklists, and Traffic Filters
5.2.5.5 Reputations, Blacklists, and Traffic Filters (Cont.)

## Slide 52: Section 5.3: Implement IPS
Upon completion of this section, you should be able to:
Understand how to configure Cisco IOS IPS with CLI
Explain how to verify and monitor IPS

## Slide 53: Topic 5.3.1: Configure Cisco IOS IPS with CLI

## Slide 54: Implement IOS IPS
Step 1. Download the IOS IPS files.
Step 2. Create an IOS IPS configuration directory in Flash.
Step 3. Configure an IOS IPS crypto key.
Step 4. Enable IOS IPS.
Step 5. Load the IOS IPS signature package to the router.
Notes: 5.3.1.1 Implement IOS IPS

## Slide 55: Download the IOS IPS Files
Notes: 5.3.1.2 Download the IOS IPS Files
5.3.1.3 IPS Crypto Key
5.3.1.4 Enable IOS IPS
5.3.1.5 Load the IPS Signature Package in RAM

## Slide 56: IPS Crypto Key
Notes: Page 5.3.1.3

## Slide 57: Enable IOS IPS
Notes: Page 5.3.1.4

## Slide 58: Enable IOS IPS
Notes: Page 5.3.1.4 (cont.)

## Slide 59: Load the IPS Signature Package in RAM
Notes: 5.3.1.5 Load the IPS Signature Package in RAM

## Slide 60: Load the IPS Signature Package in RAM
Notes: 5.3.1.5 Load the IPS Signature Package in RAM (Cont.)
5.3.1.6 Activity – Implementing IPS

## Slide 61: Retire and Unretire Signatures
Retiring an Individual Signature:
Retiring a Signature Category:
Notes: 5.3.2.1 Retire and Unretire Signatures

## Slide 62: Topic 5.3.2: Modifying Cisco IOS IPS Signatures

## Slide 63: Change Signature Actions
Notes: 5.3.2.2 Change Signature Actions

## Slide 64: Topic 5.3.3: Verify and Monitor IPS

## Slide 65: Verify IOS IPS
Show commands to verify the IOS IPS configuration:
show ip ips
show ip ips all
show ip ips configuration
show ip ips interfaces
show ip ips signatures
show ip ips statistics
Clear commands to disable IPS:
clear ip ips configuration
clear ip ips statistics
Notes: 5.3.3.1 Verify IOS IPS

## Slide 66: Report IPS Alerts
To specify the method of event notification, use the ip ips notify global configuration mode command. The log keyword sends messages in syslog format. The sdee keyword sends messages in SDEE format.
Notes: 5.3.3.2 Report IPS Alerts

## Slide 67: Enable SDEE
Notes: 5.3.3.3 Enable SDEE

## Slide 68: Section 5.4: Summary
Chapter Objectives:
Describe IPS technologies and how they are implemented.
Explain IPS Signatures.
Describe the IPS implementation process.
Notes: 5.4.1.1 Packet Tracer – Configure an IOS IPS Using CLI
5.4.1.2 Lab – Configure an IOS IPS Using CLI

## Slide 70: Instructor Resources
Remember, there are helpful tutorials and user guides available via your NetSpace home page. (https://www.netacad.com)
These resources cover a variety of topics including navigation, assessments, and assignments.
A screenshot has been provided here highlighting the tutorials related to activating exams, managing assessments, and creating quizzes.
1
2
Notes: https://www.netacad.com