## Slide 1: Cache Mapping
Bcos of cache always smaller than main memory so we need a method to map to the cache. There are three common method:-
  Direct mapping
  Full associative mapping
  Set associative mapping
Main Memory
Cache
Mapping

## Slide 2: Cache Mapping
Generally, to access computer memory is through address bus.
So, address bus width determine accessible memory number
Exp:-.
If address bus width is15 bit, the number of location that can be addressing is :-.
N = 15.
2n = location.
215= 32768.

## Slide 3: Cache Mapping
Example of how the main memory is partitioned based on the address bus width.
.
.
.
MEMORY
.
.
CPU
0
32767

## Slide 4: Cache : Direct Mapping
To allow the mapping, we have to divide the address field into two parts namely tag field & index field.
If the sytem have 2n words in main memory and 2k words in cache.
n = 15
k = 9
Tag Field Size = n - k
= 6
TAG INDEX
15 bits
TAG INDEX
15 bits
6 bits
9 bits

## Slide 5: Cache : Direct Mapping
Example
Main Memory
32K X 12
Address = 15 bits
Data = 12 bits
Cache
512 X 12
Address = 9 bits
Data = 12 bits
0
32767
0
511

## Slide 6: Cache : Direct Mapping
Main memory
0
511
0
511
0
511
.
.
.
.
12 Bits
Cache
0
63
Tag
Field
6 Bits
12 Bits
Data is stored here
Tag 0
Tag 63
Tag 1

## Slide 7: Cache : Direct Mapping
Memory
Address
Location
Tag Field
Data is stored here
Main
Memory
65
12
291
803
6 Bits
12 Bits
12 Bits
(2^15)
32767
511
Tag 0
Cache
12
Tag 0
65
Tag 1
0
??
Tag 63

## Slide 8: Address (Tag & Index)
000001100100011
000000100100011
291
803
Decimal
Form
Binary
Form
Tag Field
Index Field
Tag Field
Index Field

## Slide 9: Full Associative Mapping
Memory
Address
Location
Cache
Full address is stored here
Data is stored here
Main
Memory
65
12
291
803
15 Bits
12 Bits
12
291
65
803
12 Bits
(2^15)
32767

## Slide 10: Set Associative Mapping
0 12
Cache
Tag Value is stored here
Data is stored here
Main
Memory
65
12
291
803
2-Way Set Associative Cache
21
292
0 21
1 65
32
293
31
294
0 32
0 31