## Slide 1: Introduction to Robotics
WIA1004/WAES 1102

## Slide 2: Topics
Why are robots important?
Types of robots
Future growth areas
Technologies used in robotics
Technical disciplines needed in robotics
Sensing and Sensors

## Slide 3: What do you think of when you hear the word “robot”?
Notes:   automotive
  Dangerous, hazardous areas
  Bomb recovery
  Underwater
  Rescue
  Home

## Slide 4: Why Robotics?
Areas that robots are used:
  Industrial robots
  Military, government and space robots
  Service robots for home, healthcare, laboratory
Why are robots used?
  Dangerous tasks or in hazardous environments
  Repetitive tasks
  High precision tasks or those requiring high quality
  Labor savings
Control technologies:
  Autonomous (self-controlled), tele-operated (remote control)

## Slide 5: Industrial Robots
Uses for robots in manufacturing:
  Welding
  Painting
  Cutting
  Dispensing
  Assembly
  Polishing/Finishing
  Material Handling
    Packaging, Palletizing
    Machine loading

## Slide 6: Industrial Robots - Automotive
Notes: http://www.youtube.com/watch?v=sjAZGUcjrP8
Car Factory - Kia Sportage factory production line

## Slide 7: Industrial Robots - Packaging
Notes: http://www.youtube.com/watch?v=tMVoxMhmxEM
Mitsubishi Electric - Industrial robot: Innovative Packaging system

## Slide 8: Military/Government Robots
iRobot PackBot
Remotec Andros

## Slide 9: Military/Government Robots
Soldiers in Afghanistan being trained how to defuse a landmine using a PackBot.

## Slide 10: Military Robots
Aerial drones (UAV)
Military suit

## Slide 11: Space Robots
Mars Rovers – Spirit and Opportunity
  Autonomous navigation features with human remote control and oversight

## Slide 12: Service Robots
Many uses…
  Cleaning & Housekeeping
  Rehabilitation
  Inspection
  Agriculture & Harvesting
  Lawn Mowers
  Surveillance
  Mining Applications
  Construction
  Automatic Refilling
  Fire Fighters
  Search & Rescue
iRobot Roomba vacuum cleaner robot

## Slide 13: Medical/Healthcare Applications
  DaVinci surgical robot by Intuitive Surgical.
  St. Elizabeth Hospital is one of the local hospitals using this robot. You can see this robot in person during an open house (http://www.youtube.com/watch?v=EiVY-htgRUY)
  Japanese health care assistant suit (HAL - Hybrid Assistive Limb)
Also… Mind-controlled wheelchair using NI LabVIEW

## Slide 14: Laboratory Applications
  Drug discovery
  Test tube sorting

## Slide 15: Technologies Used in Robotics
Drivetrain – servomotors, gear reducers
Hydraulics (oil), pneumatics (air)
Electrical controls – motor drives, computers
Lightweight materials – aluminum, carbon fiber, titanium
Sensors
  Photoeyes
  Encoders/position measurement sensors
  Proximity switches
  Laser scanners
  Vision systems
  Navigation systems/GPS

## Slide 16: Disciplines Used in Robotics
Robotics merges many technical disciplines:
  Bio-Medical Engineering
  Ethics and Legal Issues
  Mechanical Engineering
  Electrical Engineering
  Computer Science
Latest advancement:
  Artificial Intelligence
Mechatronics
Intelligent
Agents

## Slide 17: Sensing and Sensors

## Slide 18: Human Sensing
Sense:
  Vision
  Audition
  Gustation
  Olfaction
  Tactile
  Thermoception
  Nociception
  Equilibrioception
  Proprioception
Sensed what?
  EM waves
  Pressure waves
  Chemicals - flavor
  Chemicals - odor
  Contact pressure
  Heat
  Pain
  Sense of balance
  Body awareness
Sensor?
  Eyes
  Ears
  Tongue
  Nose
  Skin
  Skin
  Skin, organs, joints
  Ears
  Muscles, joints

## Slide 19: Robot Sensors
Sense:
  Vision
  Audition
  Gustation
  Olfaction
  Tactitions
  Thermoception
Sensor:
  Camera
  Microphone
  Chemical sensors
  Chemical sensors
  Contact sensors
  Thermocouple

## Slide 20: Robot Sensors
Sense:
  Equilibrioception
  Proprioception
  Magnetoception
  Electroception
  Echolocation
Sensor:
  Accelerometer
  Encoders
  Magnetometer
  Voltage sensor
  Sonar

## Slide 21: Sonar Sensor
How does it detect distance?
  The sensor send out a high-frequency sound pulse and times how long it takes for the echo of the sound to be reflected back.
  The speed of sound is known, 341 m/s in air, the sensor uses rate and time to calculate distance
  Reference:
  http://learn.cs2n.org/solt/lessons/nvt2.0/content/resources/helpers/nxt_sensors/ultrasonic.html

## Slide 22: Sonar Sensor
Factors that might limit the accuracy of sonar reading:
  Object too far away
  Flat object is not facing sensor
  Object is too small
  Object is too soft

## Slide 23: Sample of robot sensors

## Slide 24: Robot Sensory Architecture

## Slide 25
B21 robot’s real world interface

## Slide 26
Robart II, by H.R. Everett
Notes: Robart II, H.R. Everett

## Slide 27
Notes: Savannah (River site nuclear surveillance robot)

## Slide 28
Pan-Tilt Camera
Omnidirectional Camera
IMU Inertial Measurement Unit
Sonar Sensors
Laser Range Scanner
Bumper
Emergency Stop Button
Wheel Encoders
BibaBot, BlueBotics SA, Switzerland

## Slide 29
Logitech QuickCam Pro 3000
  640 X 480 video; 1.3 MP still mode
Built-in microphone for sound/voice recognition applications
IR Sensors
  4 ledge detection sensors
  3 up-facing sensors
  13 horizontal facing sensors
Bump Sensor
Evolution Robotics’ Scorpion

## Slide 30
Activmedia Robotics’ PeopleBot

## Slide 31: Classification of Sensors
Proprioceptive (internal) sensors
  Measure values internally to the system (robot)
  E.g. motor speed, wheel load, heading of the robot, battery status
Exteroceptive (external) sensors
  Information from the robots environment
  Distances to objects, intensity of the ambient light, unique features

## Slide 32: Sensor Performance Measurement in real world environment is error prone
Basic sensor response ratings
  Dynamic range: Ratio between lower and upper limits, usually in decibels
  Range: Difference between min and max
  Resolution: Minimum difference between two values
  Linearity: Variation of output signal as function of the input signal
  Bandwidth or frequency: The speed with which a sensor can provide a stream of readings

## Slide 33: Sensor Performance
Mobile robots have to perceive, analyze and interpret the state of their surroundings
Measurements in real world environments are dynamically changing and error prone
Examples:
  Changing illuminations
  Specular reflections
  Light or sound absorbing surfaces
  Non adaptive to environment changes (climate (heat/damp), surface, texture, etc)

## Slide 34: Wheel/Motor Encoders

## Slide 35: Heading Sensors
Heading sensors can be proprioceptive/internal (gyroscope, inclinometer) or exteroceptive/external (compass)
Used to determine the robots orientation and inclination (slope/gradient descent)
Allow, together with appropriate velocity information, to integrate movement to a position estimate
  This procedure is called dead reckoning (ship navigation)

## Slide 36: Gyroscope
Heading sensors, that keep the orientation to a fixed frame
  Absolute measure for the heading of a mobile system
Gyroscopes are used in aeroplanes, Segways and the space shuttle and affect how yo-yos and bicycles work!
Two categories of gyroscopes
  Mechanical gyroscopes
  Optical gyroscopes
  (not covered in this lecture)

## Slide 37: Gyroscope
Concept: inertial properties of a fast spinning rotor
  Gyroscopic precession
Angular momentum associated with a spinning wheel keeps the axis of the gyroscope inertial-ly stable
Reactive torque t (tracking stability) is proportional to the spinning speed w, the precession speed W and the wheels inertia I

## Slide 38: Compass
The compass has been around since at least 2000 B.C.
  The Chinese suspended a piece of natural magnetite from a silk thread and used it to guide a chariot over land
Magnetic field on earth
  Absolute measure for orientation

## Slide 39: Compass
There are a large variety of ways to measure the earth’s magnetic field
  Mechanical magnetic compass
  Direct measure of the magnetic field (Hall-effect, magneto-resistive sensors)
Major drawback
  Weakness of the earth’s magnetic field
  Easily disturbed by magnetic objects or other sources
  Not feasible for indoor environments

## Slide 40: Beacons (ground based)
Elegant way to solve the localization problem in mobile robotics
Beacons are signaling guiding devices with a precisely known position
Beacon base navigation has been used since humans started to travel
  Natural beacons (landmarks) like stars, mountains or the sun
  Artificial beacons like lighthouses

## Slide 41: Beacons (ground based)
The recently introduced Global Positioning System (GPS) has revolutionized modern navigation technology
  Already one of the key sensors for outdoor mobile robotics
  For indoor robots GPS is not applicable
Major drawback with the use of beacons in indoor:
  Beacons require changes in the environment -> costly
  Limit flexibility and adaptability to changing environments

## Slide 42: Range Sensors
The traveled distance of a sound or electromagnetic wave is given by
d = c . t
Where
  d = distance traveled (usually round-trip)
  c = speed of wave propagation
  t = time of flight.

## Slide 43: Range Sensors
It is important to point out:
  Propagation speed of sound: ~0.3 m/ms
  Propagation speed of of electromagnetic signals: ~0.3 m/ns
  3 meters
    Takes 10ms for an ultrasonic system
    Only 10ns for a laser range sensor
    Measuring time of flight with electromagnetic signals is not an easy task
    Laser range sensors are expensive and delicate

## Slide 44: Range Sensors
The quality of time of flight range sensors mainly depends on:
  Uncertainties about the exact time of arrival of the reflected signal
  Inaccuracies in the time of fight measure (laser range sensors)
  Opening angle of transmitted beam (ultrasonic range sensors)
  Interaction with the target (surface, specular reflections)
  Variation of propagation speed
  Speed of mobile robot and target (if not at rest)

## Slide 45: Sensors Summary
Robots use sensors to sense what is going on in the world around them
Sensors can be broadly categorised as proprioceptive or exteroceptive and active or passive
Sensor error can be a serious issue that we need to take care of
There are many kinds of sensors that offer different levels of performance, error, price, etc