## Slide 1: Subprogram & Package
Chapter7

## Slide 2: Subprograms and Packages
Procedures and Functions
    Firstly, a simple example of a procedure with no parameters:
    procedure reset;
    Secondly, here is a declaration of a procedure with some parameters:
    procedure increment_reg(variable reg : inout word_32; constant incr : in integer := 1);
    A call with named association explicitly gives the formal parameter name to be associated with each actual parameter, so the parameters can be in any order. For example:
    increment_reg(incr => offset–2, reg => index_reg);
    increment_reg(reg => prog_counter);

## Slide 3: Procedures and Functions Con..
Thirdly, here is an example of function subprogram declaration:
    function byte_to_int(byte : word_8) return integer;
    For functions, the parameter mode must be in,
    If the parameter class is not specified it is assumed to be constant.
When the subprogram is called, the statements in the body are executed until either the end of the statement list is encountered, or a return statement is executed. The syntax of a return statement is:
    return_statement ::= return [ expression ] ;

## Slide 4: Functions Con..
    An example of a function body:
    function byte_to_int(byte : word_8) return integer is variable result : integer := 0; begin for index in 0 to 7 loop result := result*2 + bit'pos(byte(index)); end loop; return result; end byte_to_int;

## Slide 5: Conversion Function
Conversion functions are used to convert an object of one type to another.
For example, designer A wants to make use of an entity from designer B.
Data type of designer A:
  TYPE fourval IS (X, L, H, Z);
Data type of designer B:
    TYPE fourvalue IS (‘X’, ‘0’, ‘1’, ‘Z’)

## Slide 6: Conversion Function (Cont.)
FUNCTION convert4val (S : fourval) RETURN fourvalue IS
BEGIN
CASE S IS
WHEN X => RETURN ‘X’;
WHEN L => RETURN ‘0’;
WHEN H => RETURN ‘1’;
WHEN Z => RETURN ‘Z’;
END CASE;
END convert4val;
Conversion function can be used to synchronous both data type which is designer B accepts a value of type fourval and return a value of type fourvalue.

## Slide 7: Resolution Function
A resolution function is used to return the value of signal when the signal is driven by multiple driver.
For example, refer to the truth table below:
Two input signals will be resolution to become one output signal (e.g. combination of ‘L’ with ‘Z’ = L)

## Slide 8: Resolution Function (Cont.)
PACKAGE fourpack IS
TYPE fourval IS (X, L, H, Z);
TYPE fourval_vector IS ARRAY (natural RANGE <>) OF fourval;
FUNCTION resolve (s : fourval_vector) RETURN fourvalue;
END fourpack;
PACKAGE BODY fourpack IS
FUNCTION resolve( s: fourval_vector) RETURN fourval IS
VARIABLE result : fourval := Z;
BEGIN
FOR i IN s’RANGE LOOP
CASE result IS
WHEN Z =>
CASE s(i) IS
WHEN H => result := H;
WHEN L => result := L;
WHEN X => result := X;
WHEN OTHERS => NULL;
END CASE;

## Slide 9
WHEN L =>
CASE s(i) IS
WHEN H => result := X;
WHEN X => result := X;
WHEN OTHERS => NULL;
END CASE;
WHEN H =>
CASE s(i) IS
WHEN L => result := X;
WHEN X => result := X;
WHEN OTHERS => NULL;
END CASE;
WHEN X => result := X;
END CASE;
END LOOP;
RETURN result;
END resolve;
END fourpack;

## Slide 10: Procedures
A Procedures declaration begins with the keyword PROCEDURE followed by the procedure name and an argument list.
Procedure can be used during conversion from an array of a multivalued type to an integer.
Example in the next slide shows the procedure was converted the input argument z from array of type to an integer.

## Slide 11: Procedures
USE LIBRARY IEEE;
USE IEEE.std_logic_1164.ALL;
PROCEDURE vector_to_int (z : IN std_logic_vector; x_flag : OUT BOOLEAN; q : INOUT INTEGER) IS
BEGIN
q := 0;
x_flag := false;
FOR i IN z’RANGE LOOP
q := q * 2;
IF z(i) = ‘1’ THEN
q := q + 1;
ELSIF z(i) /= F0 THEN
x_flag := TRUE;
END IF;
END LOOP;
END vector_to_int;

## Slide 12: Packages
A package is a collection of types, constants, subprograms and possibly other things, usually intended to implement some particular service or to isolate a group of related items. In particular, the details of constant values and subprogram bodies can be hidden from users of a package, with only their interfaces made visible.
Package declaration, which defines its interface,
Package body, which defines the deferred details. The body part may be omitted if there are no deferred details.

## Slide 13: Package Declarations
An example of a package declaration:
package data_types is subtype address is bit_vector(24 downto 0); subtype data is bit_vector(15 downto 0); constant vector_table_loc : address; function data_to_int(value : data) return integer; function int_to_data(value : integer) return data; end data_types;

## Slide 14: Package Body Declarations
The body for the package data_types shown above might be written as:
package body data_types is
constant vector_table_loc : address := X"FFFF00";
function data_to_int(value : data) return integer is body of data_to_int end data_to_int;
function int_to_data(value : integer) return data is body of int_to_data end int_to_data;
end data_types;

## Slide 15: Package Use and Name Visibility
Once a package has been declared, items declared within it can be used by prefixing their names with the package name. For example, given the package declaration in last section, the items declared might be used as follows:
variable PC : data_types.address;
int_vector_loc := data_types.vector_table_loc + 4*int_level;
offset := data_types.data_to_int(offset_reg);
If all of the declared names in a package are to be used in this way, you can use the special suffix all, for example:
use data_types.all;